## Slide 1: Intrinsic Value Methodology (IVAL) A mathematical model of the human decision-making process
Dr. H. S. (Bud) Simrin
12 April 2023
Designed for slide show viewing

## Slide 2: Agenda
Introduction
Weighted Sum Model Results: Case Study
IVAL Methodology
IVAL Results for Case Study
Appendix A: Measuring Goodness of Fit of Rankings
Appendix B: Handling Dependent Criteria
Appendix C: Handling Hierarchies of Criteria
Appendix D: S-Curve Formulas
Appendix E: Exponential Curve Formulas

## Slide 3: How can one find the best from among numerous alternatives?
Example
  An aircraft company will eventually build a new fighter aircraft
  It generates 1000 candidate design alternatives
  Every design has values for 40 design criteria
    Values includes cost, weight, speed, fuel capacity, range, max altitude, etc.
  How does the company find the 10 best designs for conducting more detailed design and evaluation?
There is no physics-based formula to generate an overall value
  There are many criteria, and many are unrelated
  Soft criteria such as “design attractiveness” have no basis in physics
The heuristic Weighted Sum Model is frequently used, but …
In the absence of a truth model, how can we measure the goodness of this type of evaluation?

## Slide 4: Agenda
We conduct a hypothetical case study with only 8 designs and just 3 criteria
  We use the Weighted Sum Model
  For the case study, there is a known truth model
    It combines the criteria into an overall value
The case study shows that the Weighted Sum Model can provide substantially misleading answers
We present an alternative method that …
  Mimics the human decision-making thought process
  Generates exceptional agreement with the truth model

## Slide 5: Agenda
Introduction
Weighted Sum Model Results: Case Study
IVAL Methodology
IVAL Results for Case Study
Appendix A: Measuring Goodness of Fit of Rankings
Appendix B: Handling Dependent Criteria
Appendix C: Handling Hierarchies of Criteria
Appendix D: S-Curve Formulas
Appendix E: Exponential Curve Formulas

## Slide 6: The Weighted Sum Model (WSM)
The Task
  Compare n design alternatives
The Method
  Select design criteria and develop criterion values (xi ) for each alternative
  Assign relative weights (wi ) to criteria
  Normalize criterion values to get normalized criterion values (vi ) for each design alternative
Total Value (V) of an alternative is
V = w1v1 + w2v2 + w3v3 + … + wnvn
The alternative with the highest total value wins

## Slide 7: The Case Study
Aerospace design engineers wish to compare 8 computer-aided designs alternatives for the next-generation fighter aircraft
The criteria are all defined in terms of sorties
  A sortie is a combat flight
  Sortie rate is the number of sorties that can be flown per day
The criteria* are:
      PS = P(Aircraft Survives a Single Sortie)
      KS = Expected Number of Target Kills per Sortie
      SR = Planned (Expected) Sortie Rate
  PS is a metric for defense
  KS is a metric for offense
  SR represents the frequency of events
* Cost is always included in military effectiveness analyses but is omitted in this case study to keep the study as simple as possible

## Slide 8: The Data
Questions
  Which of first 4 aircraft designs is best?
  Which of second 4 aircraft designs is best?
  Which is best overall?
Aircraft | SR | PS | KS | Rating
1 | 10.0 | 0.99 | 0.1 | ?
2 | 10.0 | 0.30 | 10.0 | 
3 | 0.1 | 0.99 | 10.0 | 
4 | 5.0 | 0.95 | 5.0 | 
5 | 1.0 | 0.98 | 5.0 | 
6 | 5.0 | 0.98 | 3.0 | 
7 | 7.0 | 0.95 | 3.0 | 
8 | 3.0 | 0.95 | 7.0 | 
Note : In all cases, larger criterion values are better

## Slide 9: Using Intuition To Compare The First 4 Combat Aircraft Designs
Designs 1-3 are unacceptable
  No. 1 has superb SR and Survivability but carries virtually no weapons (10 flights to kill 1 target!!!)
  No. 2 has superb SR and Effectiveness but is not survivable (only 9% left after 2 days!!!)
  No. 3 has superb Survivability and Effectiveness but rarely is able to fly (only 1 sortie in 10 days!!!)
Design No. 4 is a reasonable, balanced design even though it doesn’t excel in any particular category
Aircraft | SR | PS | KS
1 | 10.0 | 0.99 | 0.1
2 | 10.0 | 0.30 | 10.0
3 | 0.1 | 0.99 | 10.0
4 | 5.0 | 0.95 | 5.0

## Slide 10: Weighted Sum Model Approach and Results
Aircraft |  |  |  | Weights and Normalized Criterion Value |  |  |  |  |  | Total Value
No. | SR | PS | KS | w1 | V(SR) | w2 | V(PS) | w3 | V(KS) | 100 x V
1 | 10.0 | 0.99 | 0.1 |  |  |  |  |  |  | 
2 | 10.0 | 0.30 | 10.0 |  |  |  |  |  |  | 
3 | 0.1 | 0.99 | 10.0 |  |  |  |  |  |  | 
4 | 5.0 | 0.95 | 5.0 |  |  |  |  |  |  | 
Aircraft |  |  |  | Weights and Normalized Criterion Value |  |  |  |  |  | Total Value
No. | SR | PS | KS | w1 | V(SR) | w2 | V(PS) | w3 | V(KS) | 100 x V
1 | 10.0 | 0.99 | 0.1 | 0.25 |  | 0.50 |  | 0.25 |  | 
2 | 10.0 | 0.30 | 10.0 | 0.25 |  | 0.50 |  | 0.25 |  | 
3 | 0.1 | 0.99 | 10.0 | 0.25 |  | 0.50 |  | 0.25 |  | 
4 | 5.0 | 0.95 | 5.0 | 0.25 |  | 0.50 |  | 0.25 |  | 
Aircraft |  |  |  | Weights and Normalized Criterion Values |  |  |  |  |  | Total Value
No. | SR | PS | KS | w1 | V(SR) | w2 | V(PS) | w3 | V(KS) | 100 x V
1 | 10.0 | 0.99 | 0.1 | 0.25 | 1.00 | 0.50 | 0.99 | 0.25 | 0.01 | 
2 | 10.0 | 0.30 | 10.0 | 0.25 | 1.00 | 0.50 | 0.30 | 0.25 | 1.00 | 
3 | 0.1 | 0.99 | 10.0 | 0.25 | 0.01 | 0.50 | 0.99 | 0.25 | 1.00 | 
4 | 5.0 | 0.99 | 5.0 | 0.25 | 0.50 | 0.50 | 0.95 | 0.25 | 0.50 | 
Aircraft |  |  |  | Weights and Normalized Criterion Value |  |  |  |  |  | Total Value
No. | SR | PS | KS | w1 | V(SR) | w2 | V(PS) | w3 | V(KS) | 100 x V
1 | 10.0 | 0.99 | 0.1 | 0.25 | 1.00 | 0.50 | 0.99 | 0.25 | 0.01 | 74.8
2 | 10.0 | 0.30 | 10.0 | 0.25 | 1.00 | 0.50 | 0.30 | 0.25 | 1.00 | 65.0
3 | 0.1 | 0.99 | 10.0 | 0.25 | 0.01 | 0.50 | 0.99 | 0.25 | 1.00 | 74.8
4 | 5.0 | 0.95 | 5.0 | 0.25 | 0.50 | 0.50 | 0.95 | 0.25 | 0.50 | 72.5
The winners
The winners
Typical weights:
.25, .50, .25
Typical weights:
.25, .50, .25
Typical weights:
.25, 50, .25
Assign relative weights w1 ,w2 , and w3 , to SR, PS, and KS
Normalize the Criterion Values to all be between 0 and 1
Compute Total Value: V = w1 V(SR) + w2 V(PS) + w3 V(KS)

## Slide 11: Changing Weights Doesn’t Help
No matter what weights are chosen …
  The balanced design never emerges, as it should, as overwhelmingly better than the unacceptable designs
  In fact, one or more of the unacceptable designs always emerges as not only viable but as the preferred choice!!!
Notes: Double click on figures. Excel spreadsheet opens up. Enter weights for Configuration1 (and spreadsheet populates the same weights for the others) and exit back to ppt.
Basically, the reason other weighting factors also favor unacceptable configurations is that if you increase any weight, then at least one of the unacceptable configurations increases its value.

## Slide 12: Let’s Examine a Truth Model
A Truth Model is an equation that gives the “correct” answers
  Ideally, it should represent the exact truth
  In practice, it may be just a very good approximation
  It is the standard against which all other results are compared
Our Truth Model is exact:
  K = Number of targets killed in 10 days of combat
  This is known as the Fundamental Equation of Combat Aircraft Survivability*
* Developed by Gordon B. Dobbins, Jr. at Lockheed-Martin Aerospace Company in the 1980’s
  Key observation: This relationship between criteria is highly nonlinear

## Slide 13: Comparing Weighted Sum Model Equation to Truth Model
Color Codes: Red = Poor Design
Yellow = Mediocre
Green = Excellent
Truth Model
Weighting- Factor Total Value
Weighted Sum Model Fails To Distinguish Between excellent and poor, a factor of ten different

## Slide 14: Using Intuition To Compare Balanced Designs 4 - 8
Aircraft | SR | PS | KS
4 | 5.0 | 0.95 | 5.0
5 | 1.0 | 0.98 | 5.0
6 | 5.0 | 0.98 | 3.0
7 | 7.0 | 0.95 | 3.0
8 | 3.0 | 0.95 | 7.0
Aircraft | SR | PS | KS
4 | Good | Poor | Good
5 | Poor | Mediocre | Good
6 | Good | Mediocre | Mediocre
7 | Excellent | Poor | Mediocre
8 | Mediocre | Poor | Excellent
2nd table interprets the criterion values
Very difficult to rank order using just intuition

## Slide 15: Weighted Sum Model Results For The 5 Feasible Designs
Red = Poor Design, Yellow = Mediocre, Green = Excellent
Peanut-Butter Spread
Weighted Sum Model Fails To Identify the Three Excellent Designs
    In Appendix A it is shown that these WSM results have a .58 correlation with the Fundamental Equation, a seemingly good correlation
    These random-like results indicate that a much higher correlation coefficient is needed to achieve a successful ranking study
Notes: It is difficult to use intuition to rank 4-8 because each has one value the same, one better, and one worse than Config 4.
However, the Fundamental Eq uncovers the true worth
Notice that the Fund Eqgroups 5 & 7 together as low, and 4, 6, and 8 as high.
WSM does correctly ID 5 as the worst (although the value is too high)
However, it altogether fails to distinguish #7 as a poor choice
Moreover, none of these reasonable designs outscored flawed designs 1 and 3!

## Slide 16: Why Does WSM Perform So Poorly?
WSM is a linear scheme
  Linear approximations of non-linear systems have a narrow range of validity
  Think of a tangent line to a circle
  Weighting factors don’t behave as expected
    When there are many criteria, all of the weights are small and each criterion has only a small contribution to the total value
    There can be at most one critical criterion
      Lack of capability in a critical criterion will not eliminate an alternative
Without a truth equation there can be little certainty about WSM rankings
Notes: Compensatory Models. A multi-criterion model in which one criterion compensates for another
Example: Select an inexpensive apartment in a quiet neighborhood even though it is located far from school. The cost and quiet criteria compensate for the location criterion.
Compensatory vs non-compensatory models might be discussed in a business model development course.
Compensatory and non-compensatory refer to models in which criteria are compared against each other. IVAL is neither compensatory nor non-compensatory because criteria are not compared against each other.

## Slide 17: Agenda
Introduction
Weighted Sum Model Results: Case Study
IVAL Methodology
IVAL Results for Case Study
Appendix A: Measuring Goodness of Fit of Rankings
Appendix B: Handling Dependent Criteria
Appendix C: Handling Hierarchies of Criteria
Appendix D: S-Curve Formulas
Appendix E: Exponential Curve Formulas

## Slide 18: Introducing Intrinsic Value Methodology (IVAL) …
An approach that uses mathematics to model the human decision making process
  As simple as the Weighted Sum Model
  Avoids the weaknesses of the Weighted Sum Model
IVAL relaces weighting factors by curves
The curves generate IVAL factors
The IVAL factors are multiplied to generate total value

## Slide 19: IVAL Curves Use Just 3 Features To Mimic Human Decision-Making Process
  Steep region
  Flat region(s)
  Floor
These identify the regions of diminishing returns, escalating returns, and the importance of the criterion
IVAL Factor
0
1
vi
xi (Criterion i)

## Slide 20: Explaining the Three Features
  Steep regions
  Where small changes in criterion value are very important
  Flat regions
    Where even large changes in criterion value do not much matter
    For example, a 500 mile radar is not more useful than a 80 mile radar if a missile can only fly 50 miles
  Floor reflects a criterion’s intrinsic importance (i.e., “weight”)
    Critical criteria have floors near zero
      Because V = v1• v2 • v3 • … • vn , a low score in any critical criterion yields a near-zero total value V
    “Nice-to-have” criteria have floors closer to 1.0
      A low score does not unduly lower the total value

## Slide 21: Example of the Three Features: Radar Range
To take full advantage a 50 NM missile, a radar would need a range of at least 60 NM
The opponent that launches first has the advantage
But, there would be little payoff beyond, say, 80 NM because the missile would be launched at 50 NM
So there is steep design benefit from, say, 60 – 80 NM
We would set the knees of the curve at 60 and 80
There are flat regions on either side, with only incremental benefits
  Too little range has no benefit
  Too much range does not help
Radar Range Score
0
1
0
300
Radar Range (ui)
vi
Radar Range Score
0
1
0
300
Radar Range (ui)
vi
70

## Slide 22: Typical IVAL Curves
Increasing
Decreasing
Exponential (1 knee)
S-Curve (2 knees)
Linear
We recommend using 20/80 for knees of curves
Appendices provide equation templates
IVAL accommodates curves of any shape
.80
.20
.80
.20
.80
.20

## Slide 23: Intrinsic Value Methodology (IVAL) Has Just Three Steps
  Define intrinsic-value curves
    Focus on steep regions, flat regions, and floors
      Lines (all regions have same flatness, same steepness)
      Simple exponentials (1 flat region, 1 steep region)
      S-curves (2 flat regions, 1 steep region)
    Use Curves to generate IVAL factors for alternatives
      IVAL Factor = vi = fi(xi) for each (aircraft) criterion xi
    Multiply the IVAL factors to obtain a total value for each (aircraft) alternative: V = v1• v2• v3• … • vn
Criterion 1
Criterion 2
Criterion 3
v1
v2
v3

## Slide 24: Agenda
Introduction
Weighted Sum Model Results: Case Study
IVAL Methodology
IVAL Results for Case Study
Appendix A: Measuring Goodness of Fit of Rankings
Appendix B: Handling Dependent Criteria
Appendix C: Handling Hierarchies of Criteria
Appendix D: S-Curve Formulas
Appendix E: Exponential Curve Formulas

## Slide 25: Step 1: Define the curves for the case study
IVAL Factor
0
0.0
0.8
1.0
0.2
6
Value
Sortie Rate
1
IVAL Factor
0.0
0.0
1.0
0.5
0.98
Value
Probability of Survival
0.92
0.95
0.9
1.0
A = 0.01661
B = 1.2672
x
1-x
B
v = 1-e-A
v = x
A = 0.22314
B = 1.1027
v = 1-e-AxB
IVAL Factor
0
0
10
10
Value
Kills per Sortie
SR
PS
KS
Subject Matter Experts generate curves that represents each criterion’s contribution to the total value
Typically curves are lines, exponentials, or S” curves, but any shape is allowed

## Slide 26: Step 2: Use Curves to Generate IVAL Factors
Red = Poor Design, Yellow = Mediocre, Green = Excellent
IVAL Factors come from plugging Configuration Values into IVAL curves

## Slide 27: Step 3: Compute Total Values
Red = Poor Design, Yellow = Mediocre, Green = Excellent
IVAL Results Match Truth Model Very Closely*
Total Value scaled by 50 for easier visual comparison
* Pearson r Correlation Coefficient is 0.99

## Slide 28: There are rank reversals even at 99% correlation
Red = Poor Design, Yellow = Mediocre, Green = Excellent
Total Value scaled by 50 for easier visual comparison
By Truth Model, #8 is clearly best, followed by #6
By IVAL, #6 is clearly best, followed by #8
A very high correlation is needed for ranking

## Slide 29: Examining Larger Design Spaces
Consider a narrow, medium and wide design space
Each design space has a full factorial 27 alternatives consisting of (3 sortie rates) x (3 PS’s) x (3 KS’s)
  Narrow SR: 1 – 3 PS: .97 – .99 KS: 1 – 3
  Medium SR: 1 – 5 PS: .94 – .99 KS: 1 – 5
  Wide SR: 1 – 9 PS: .91 – .99 KS: 1 – 9
 | Pearson r Correlation Coefficient (Output) |  |  |  | 
 | Original 8 Designs | Only the 5 Feasible Designs | Narrow design space | Medium design space | Wide design space
WSM | .038 | .584 | .979 | .897 | .736
IVAL | .987 | .949 | .996 | .986 | .985
The next chart explains how correlation coefficients relate to the fidelity of ranking
Notes: Subject matter experts (SME)
  (either by engineering or by judgment)

## Slide 30: How Correlation Coefficients Relate To Ability To Identify Top 10% of Alternatives
Correlation Coefficient | Percent of top 10% Identified
.95 | 100%
.90 | 67%
.75 | 33%
Top 10% of ranked alternatives include
  all of the Truth Model’s top 10% when correlation is .95
  2/3 of the Truth Model’s top 10% when correlation is .90
  1/3 of the Truth Model’s top 10% when correlation is .75
Rank order of top 10% differs from Truth Model more and more as correlation drops
  Even .99 correlation includes some rank reversals
  .995 correlation is required to entirely avoid rank reversals
.95 correlation is needed in order to correctly identify the top 10%

## Slide 31: IVAL Results Are Consistently Superior To WSM Over Wide Range of Case Studies
 | Pearson r Correlation Coefficient (Output) |  |  |  | 
 | Original 8 Designs | Only the 5 Feasible Designs | 27 A/C (narrow design space) | 27 A/C (medium design space) | 27 A/C (wide design space)
WSM | .038 | .584 |  |  | 
IVAL | .987 | .949 |  |  | 
WSM cannot be relied upon to find the top candidates
IVAL always identifies the top Truth Model candidates
 | Pearson r Correlation Coefficient (Output) |  |  |  | 
 | Original 8 Designs | Only the 5 Feasible Designs | 27 A/C (narrow design space) | 27 A/C (medium design space) | 27 A/C (wide design space)
WSM | .038 | .584 | .979 | .897 | .736
IVAL | .987 | .949 | .996 | .986 | .985

## Slide 32: Why IVAL performs well
IVAL is a multiplicative scheme
  Poor performance in any important criterion generates a near-zero multiplicative factor (since floor is near zero)
IVAL factors are intrinsic rather than relative to other criteria
  “Intrinsic” means that an IVAL factor represents how criterion affects the total value
  Intrinsic values reflect a criterion’s criticality
    They impose heavy penalty for a poor value in a critical criterion
    They impose light penalties for a poor value in other criteria
IVAL curves represent decision-makers’ values
  Steep Region: nearby criterion values yield dissimilar outcomes
  Flat Region(s): distant criterion values yield similar outcomes
  Floor: the “absolute weight” of a criterion

## Slide 33: Comparing WSM and IVAL Thought Process
In WSM, criteria are compared to each other
  Weights are assigned to signify relative importance
  For example, we may assign Survivability twice the weight of Lethality
  At most one criterion can have a weight of more than .50
  At most one criterion will score as “critical”
With IVAL, criteria are not compared to each other
  Rather, each criterion is examined for its contribution to the total value
  For example, we don’t ask if Survivability is twice as important as Lethality
  Rather, we ask how Survivability affects the total value
  If several criteria are critical, each one will have a large impact

## Slide 34: WSM and IVAL Steps Are Similar
WSM
  Step 1: Develop criterion relative weights wi
  Step 2: Generate criterion normalized values vi (for each alternative)
  Step 3. Add to get total value between 0 and 1 (for each alternative)
  V = w1v1 + w2v2 + w3v3 + … + wnvn
    Total value starts at 0 and increases as you add terms
IVAL
  Step 1: Develop IVAL curves
  Step 2: Use curves to generate IVAL factors vi (for each alternative)
  Step 3. Multiply to get total value between 0 and 1 (for each alternative)
  V = v1 • v2 • v3 • … • vn
    Total value starts at 1 and decreases as you multiply factors

## Slide 35: Summary
Weighted Sum Model (WSM)
  Widely used and trusted
  Very easy to implement
  Always provides answers
  Goodness of rankings is uncertain
  Correlation varied from 0.04 to 0.95 in case studies
Intrinsic Value Methodology (IVAL)
  A one-for-one (coding) replacement for WSM
  High confidence in goodness of rankings
  Ever so slightly more complex equation
  Much easier to use
    No need to do pairwise criteria comparisons
  Correlation varied from 0.95 to 0.997 in case studies
Notes: For example, WSM plays a central role in the Quality Function Deployment (QFD) House of Quality
Thus, if WSM is flawed, the House of Quality is also flawed, from the foundation on up.
IVAL can be substituted for WSM in an alternate derivation of the House of Quality

## Slide 36: Appendices
Goodness of Fit Equations (Pearson-r Correlation Coefficient)
Equations for increasing and decreasing S-curves and exponentials, covering when domains are
  Closed interval
  Infinite interval
Handling of 2 (or more) correlated criteria
  For example, how many weapons a fighter is designed to carry is highly correlated with how far the plane can fly
  Including both as full factors constitutes double accounting
Handling hierarchies of criteria (as in Analytic Hierarchy Process, AHP)
Issues #3 and #4 are very simple to include in IVAL

## Slide 37: Agenda
Introduction
Weighted Sum Model Results: Case Study
IVAL Methodology
IVAL Results for Case Study
Appendix A: Measuring Goodness of Fit of Rankings
Appendix B: Handling Dependent Criteria
Appendix C: Handling Hierarchies of Criteria
Appendix D: S-Curve Formulas
Appendix E: Exponential Curve Formulas

## Slide 38: Goodness of Fit of Rankings 〜 Pearson’s r Correlation Coefficient 〜
Let X be the random variable representing the Truth Model distribution
Let Y be the random variable representing the distribution of WSM (or any other ranking scheme to be compared)
Pearson’s r Correlation Coefficient is defined as
Ranges from -1 to +1
Inverse Correlation | - 1
Uncorrelated | 0
Perfect Correlation | +1

## Slide 39: Pearson r Correlation Coefficients
WSM validity varies
Without a truth model there is no way to know
IVAL is consistent across studies tested
 | Pearson r Correlation Coefficient (Output) |  |  |  | 
 | Original 8 Designs | Only the 5 Feasible Designs | 27 A/C (narrow design space) | 27 A/C (medium design space) | 27 A/C (wide design space)
WSM | .038 | .584 | .979 | .897 | .736
IVAL | .987 | .949 | .996 | .986 | .985

## Slide 40: Agenda
Introduction
Weighted Sum Model Results: Case Study
IVAL Methodology
IVAL Results for Case Study
Appendix A: Measuring Goodness of Fit of Rankings
Appendix B: Handling Dependent Criteria
Appendix C: Handling Hierarchies of Criteria
Appendix D: S-Curve Formulas
Appendix E: Exponential Curve Formulas

## Slide 41: Treatment of Two Correlated Criteria
Two criteria can be fully dependent, partially dependent, or independent
Suppose Y = v1 v2 v3 v4
Assume criteria 3 and 4 are fully dependent; i.e., v3 = v4
  Were we to use the above equation for this situation, we would get Y = v1 v2 v3 v4 = v1 v2 v32
  v3 would be double-accounted
  Y = v1 v2 v3 is more appropriate
If two criteria are fully dependent, then taking square root of each provides proper representation

## Slide 42: Extending to Treatment of Partially Dependent and Independent
.75
1
.875
.625
.5
Fully Dependent:
  Exponents of ½
  Y = v1 v2 v30.5 v40.5
Moderately Dependent:
  Exponents of ¾
  Y = v1 v2 v3.75 v4.75
Weakly/Strongly Dependent:
  Split difference again
Independent:
  Exponents of 1
  Y = v1 v2 v3 v4
Exponent
Independent
Strongly dependent
Weakly dependent
Moderately dependent
Dependent

## Slide 43: Treatment of Three Correlated Criteria
Extreme example: Three of five criteria are fully dependent (i.e., equal): Ps, Pk, SR, SR, and SR.
  The correct answer is Y = v1 v2 v3 , which we rewrite as
    Y = v1 v2 v31/3 v41/3 v51/3
Completely Dependent – Give each criterion an exponent of 1/3
Dependent | 0.333
Independent | 1.000
Dependent | 0.333
Moderately Dependent | 0.667
Independent | 1.000
Dependent | 0.333
Mostly Dependent | 0.500
Moderately Dependent | 0.667
Slightly Dependent | 0.833
Independent | 1.000

## Slide 44: Treatment of Four Inter-related Criteria
Dependent | 
Independent | 1.000
Examples:
  Y = v1 v2 v3.25 v4.25 v5.25 v6.25 (completely dependent)
  Y = v1 v2 v3.625 v4.625 v5.625 v6.625 (moderately dependent)
Dependent | 0.250
Independent | 1.000
Dependent | 0.250
Moderately Dependent | 
Independent | 1.000
Dependent | 0.250
Moderately Dependent | 0.625
Independent | 1.000
Dependent | 0.250
Mostly Dependent | 
Moderately Dependent | 0.625
Slightly Dependent | 
Independent | 1.000
Dependent | 0.250
Strongly Dependent | 0.4375
Moderately Dependent | 0.625
Weakly Dependent | 0.8125
Independent | 1.000

## Slide 45: IVAL Equation With Treatment For Dependencies – General Case
  i = 1, 2, 3, …, n
  vi = IVAL factor
  qi = Correlation exponent of criterion i
  Y = Total value for the alternative

## Slide 46: Agenda
Introduction
Weighted Sum Model Results: Case Study
IVAL Methodology
IVAL Results for Case Study
Appendix A: Measuring Goodness of Fit of Rankings
Appendix B: Handling Dependent Criteria
Appendix C: Handling Hierarchies of Criteria
Appendix D: S-Curve Formulas
Appendix E: Exponential Curve Formulas

## Slide 47: Treatment of Hierarchies of Criteria
Criterion Z is composed of Criteria A – C
Criterion A is composed of Criteria A1 – A3
Criterion B is composed of Criteria B1 – B3
Criterion C is composed of Criteria C1 – C3
Total values are first computed for A, B, and C
“q” exponents are correlation exponents as developed in Appendix B
Then, Z total value is computed from A – C

## Slide 48: Agenda
Introduction
Weighted Sum Model Results: Case Study
IVAL Methodology
IVAL Results for Case Study
Appendix A: Measuring Goodness of Fit of Rankings
Appendix B: Handling Dependent Criteria
Appendix C: Handling Hierarchies of Criteria
Appendix D: S-Curve Formulas
Appendix E: Exponential Curve Formulas

## Slide 49: Overview of the S-curve Formulas
In this appendix, formulas for four generic S-curves are developed: increasing or decreasing, and defined on a closed interval [a, b] or a half-open interval [a, ∞).
In the general formula, no restriction is placed on the floor or even on the upper bound (on the y-axis).
The knee of the curve is often represented by either 20% - 80% or else 30% - 70%. We provide formulas for the y-value in the 20/80 case. The 30/70 or any other case is easy to generate following this pattern.
A common choice for the upper bound is unity. Consequently, formulas are provided for this special case.
For critical criteria, the floor is usually set to zero. So, formulas are also provided for the special case of a floor of zero and an upper bound of unity.

## Slide 50: S-Curve Formulas
Case 1: Infinite Interval [a, )
Increasing Function
Givens
(x1, y1) = Point of Lower Diminishing Returns
(x2, y2) = Point of Upper Diminishing Returns
a = Lower Bound for Criterion Value
c = Lower Bound for IVAL Factor
d = Upper Bound for IVAL Factor
Solution
y = c + (d – c) [ 1 – e-A (x – a)B], x  a
where
B =
In [In (d – c) – In (d – y2)] – In [ln (d – c) – In (d – y1)]
In (x2 – a) – ln (x1 – a)
A =
In (d – c) – In (d – y1)
(x1 – a) B
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
c
y1
y2
d
y1 = c + .2 (d – c)
y2 = c + .8 (d – c)
20%-80% Inflection points:
Notes: A superior approach is to use Cubic Splines (Charles McLane)

## Slide 51: S-Curve Formulas
Case 1a: Upper bound of unity
Givens
(x1, y1) = Point of Lower Diminishing Returns
(x2, y2) = Point of Upper Diminishing Returns
a = Lower Bound for Criterion Value
c = Lower Bound for IVAL Factor
1 = Upper Bound for IVAL Factor
Solution
y = c + (1– c) [ 1 – e-A (x – a )B], x  a
where
B =
In [In (1– c) – In (1 – y2)] – In [ln (1– c) – In (1 – y1)]
In (x2 – a) – ln (x1 – a)
A =
In (1– c) – In (1 – y1)
(x1 – a) B
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
c
y1
y2
1
y1 = .8 c + .2
y2 = .2 c + .8
20%-80% Inflection points:
Notes: A superior approach is to use Cubic Splines (Charles McLane)

## Slide 52: S-Curve Formulas
Case 1b: [c, d] = [0, 1]
Knees of Curve at 0.2 and 0.8
Givens
(x1, 0.2) = Point of Lower Diminishing Returns
(x2, 0.8) = Point of Upper Diminishing Returns
a = Lower Bound for Criterion Value
c = 0 = Lower Bound for IVAL Factor
d = 1 = Upper Bound for IVAL Factor
Solution
y = 1 – e-A (x – a)B, x ≥ a
where
B =
ln
ln 5
A =
In 1.25
(x1 – a)B
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
0.2
0.8
1
ln 1.25
ln
x2 - a
x1 - a

## Slide 53: S-Curve Formulas
Case 2: Infinite Interval [a, )
Decreasing Function
Givens
(x1, y1) = Point of Upper Diminishing Returns
(x2, y2) = Point of Lower Diminishing Returns
a = Lower Bound for Criterion Value
c = Lower Bound for IVAL Factor
d = Upper Bound for IVAL Factor
Solution
y = c + (d – c) e-A (x – a) B, x  a
where
B =
In [In (d – c) – In (y2 – c)] – In [In (d – c) – In (y1 – c)]
In – ln (x1 – a) (x2 – a)
A =
In (d – c) – In (y1 – c)
(x1 – a)B
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
c
y2
y1
d
y2 = c + .2 (d – c)
y1 = c + .8 (d – c)
20%-80% Inflection points:

## Slide 54: S-Curve Formulas
Case 2a: Upper bound of unity
Givens
(x1, y1 ) = Point of Upper Diminishing Returns
(x2, y2 ) = Point of Lower Diminishing Returns
a = Lower Bound for Criterion Value
c = Lower Bound for IVAL Factor
1 = Upper Bound for IVAL Factor
Solution
y = c + (1– c) e-A (x – a)B, x ≥ a
where
B =
In [In (1– c) – In (y2 – c)] – In [In (1– c) – In (y1 – c)]
In (x2 – a) – ln (x1 – a)
A =
In (1– c) – In (y1 – c)
(x1 – a)B
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
c
y2
y1
1
y2 = .8 c + .2
y1 = .2 c + .8
20%-80% Inflection points:

## Slide 55: S-Curve Formulas
Case 2b: [c, d] = [0, 1]
Knees of Curve at 0.8 and 0.2
Givens
(x1, 0.8) = Point of Upper Diminishing Returns
(x2, 0.2) = Point of Lower Diminishing Returns
a = Lower Bound for Criterion Value
c = 0 = Lower Bound for IVAL Factor
d = 1 = Upper Bound for IVAL Factor
Solution
y = e-A (x – a)B, x ≥ a
where
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
0.2
0.8
1
B =
ln
ln 5
A =
In 1.25
(x1 – a) B
ln 1.25
ln
x2 - a
x1 - a

## Slide 56: S-Curve Formulas
y = c + (d – c) [ 1 – e- A ], a ≤ x ≤ b
ln [In (d – c) – ln (d – y2)] – ln [ln (d – c) – ln (d – y1)]
[ln (b – x1) – ln (x1 – a)] – [ln (b – x2) – ln (x2 – a)]
x – a B
In (d – c) – In (d – y1)
b – x1
x1 – a B
Case 3: Finite Interval [a, b]
Increasing Function
Givens
(x1, y1 ) = Point of Lower Diminishing Returns
(x2, y2) = Point of Upper Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = Lower Bound for IVAL Factor
d = Upper Bound for IVAL Factor
Solution
where
B =
A =
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
c
y1
y2
d
b
y1 = c + .2 (d – c)
y2 = c + .8 (d – c)
20%-80% Inflection points:
b – x

## Slide 57: S-Curve Formulas
b – x
y = c + (1– c) [ 1 – e-A ], a ≤ x ≤ b
ln [In (1– c) – ln ((1 – y2)] – ln [ln (1– c) – ln (1 – y1)]
[ln (b – x1) – ln (x1 – a)] – [ln (b – x2) – ln (x2 – a) ]
x – a B
In (1– c) – In (1 – y1)
b – x1
x1 – a B
Case 3a: Upper bound of unity
Givens
(x1, y1) = Point of Lower Diminishing Returns
(x2, y2) = Point of Upper Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = Lower Bound for IVAL Factor
1 = Upper Bound for IVAL Factor
Solution
where
B =
A =
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
c
y1
y2
1
b
y1 = .8 c + .2
y2 = .2 c + .8
20%-80% Inflection points:

## Slide 58: S-Curve Formulas
x – a
b – x
b – x1
x2 – a
x1 – a
In 5
ln 1.25
b – x1
b – x2
x1 – a B
Case 3b: [c, d] = [0, 1]
Knees of Curve at 0.2 and 0.8
Givens
(x1, 0.2) = Point of Lower Diminishing Returns
(x2, 0.8) = Point of Upper Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = 0 = Lower Bound for IVAL Factor
d = 1 = Upper Bound for IVAL Factor
Solution
y = 1 – e , a ≤ x ≤ b
where
B =
-A
A =
ln 1.25
IVAL Factor (y)
a
x1
x2
0
0.2
0.8
1
ln
B
b
ln
Criterion Value (x)

## Slide 59: S-Curve Formulas
y = c + (d – c) e-A , a ≤ x ≤ b
x – a B
b – x
Case 4: Finite Interval [a, b]
Decreasing Function
Givens
(x1, y1) = Point of Upper Diminishing Returns
(x2, y2) = Point of Lower Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = Lower Bound for IVAL Factor
d = Upper Bound for IVAL Factor
Solution
where
B =
ln [In (d - c) – ln (y2 - c )] – ln [ln (d - c) – ln (y1 - c)]
[ln (b - x1) – ln (x1 - a)] – [ln (b - x2) – ln (x2 - a)]
A =
In (d - c) – In (y1 - c)
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
c
y2
y1
d
b - x1
x1 - a B
b
y2 = c + .2 (d – c)
y1 = c + .8 (d – c)
20%-80% Inflection points:

## Slide 60: S-Curve Formulas
b – x
Case 4a: Upper bound of unity
Givens
(x1, y1 ) = Point of Upper Diminishing Returns
(x2, y2) = Point of Lower Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = Lower Bound for IVAL Factor
1 = Upper Bound for IVAL Factor
Solution
y = c + (1 – c) e-A , a ≤ x ≤ b
where
B =
ln [In (1 - c) – ln (y2 - c )] – ln [ln (1 - c) – ln (y1 - c)]
[ln (b - x1) – ln (x1 - a)] – [ln (b - x2) – ln (x2 - a)]
A =
In (1 - c) – In (y1 - c)
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
c
y2
y1
1
x – a B
b - x1
x1 - a B
b
y2 = .8 c + .2
y1 = .2 c + .8
20%-80% Inflection points:

## Slide 61: S-Curve Formulas
b  x1
x2 – a
x1 – a
In 5
ln 1.25
b – x1
b – x2
x1  a B
x – a
b – x
Case 4b: [c, d] = [0, 1]
Knees of Curve at 0.8 and 0.2
Givens
(x1, 0.8) = Point of Upper Diminishing Returns
(x2, 0.2) = Point of Lower Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = 0 = Lower Bound for IVAL Factor
d = 1 = Upper Bound for IVAL Factor
Solution
y = e , a ≤ x ≤ b
where
Criterion Value (x)
IVAL Factor (y)
a
x1
x2
0
0.2
0.8
1
B =
A =
ln 1.25
ln
b
- A
B
ln

## Slide 62: S-Curve Note
In order for equations 1 – 4 to represent “S” shapes, the following must be true:
  A > 0
  B > 1
It is OK to use other values
Just be aware that the curve will not be S shaped

## Slide 63: Agenda
Introduction
Weighted Sum Model Results: Case Study
IVAL Methodology
IVAL Results for Case Study
Appendix A: Measuring Goodness of Fit of Rankings
Appendix B: Handling Dependent Criteria
Appendix C: Handling Hierarchies of Criteria
Appendix D: S-Curve Formulas
Appendix E: Exponential Curve Formulas

## Slide 64: Exponential Curve Formulas
Case 1: Infinite Interval [a, )
Increasing Function
Givens
(x1, y1 ) = Point Diminishing Returns
a = Lower Bound for Criterion Value
c = Lower Bound for IVAL Factor
d = Upper Bound for IVAL Factor
Solution
y = d – (d – c) e-A (x – a), x ≥ a
A =
In (d – c) – ln (d – y1)
x1 – a
IVAL Factor (y)
a
x1
0
c
y1
d
where
Criterion Value (x)

## Slide 65: Exponential Curve Formulas
Case 1a: Upper bound of unity
Givens
(x1, y1 ) = Point Diminishing Returns
a = Lower Bound for Criterion Value
c = Lower Bound for IVAL Factor
1 = Upper Bound for IVAL Factor
Solution
y = 1 – (1– c) e-A (x – a), x ≥ a
A =
In (1– c) – ln (1 – y1)
x1 – a
Criterion Value (x)
IVAL Factor (y)
a
x1
0
c
y1
1
where

## Slide 66: Exponential Curve Formulas
In 5
x1 – a
A04-12368121
Case 1b: [c, d] = [0, 1]
Knee of Curve at 0.8
Givens
(x1, 0.8) = Point of Diminishing Returns
a = Lower Bound for Criterion Value
c = 0 = Lower Bound for IVAL Factor
d = 1 = Upper Bound for IVAL Factor
Solution
y = 1 – e-A (x – a), x ≥ a
where
A =
Criterion Value (x)
IVAL Factor (y)
a
x1
0
0.8
1

## Slide 67: Exponential Curve Formulas
Case 2: Infinite Interval [a, )
Decreasing Function
Givens
(x1, y1 ) = Point of Diminishing Returns
a = Lower Bound for Criterion Value
c = Lower Bound for IVAL Factor
d = Upper Bound for IVAL Factor
Solution
y = (d – c) e-A (x – a), x ≥ a
where
Criterion Value (x)
IVAL Factor (y)
a
x1
0
c
y1
d
A =
In (d – c) – ln y1
x1 – a

## Slide 68: Exponential Curve Formulas
Case 2a: Upper bound of unity
Givens
(x1, y1 ) = Point of Diminishing Returns
a = Lower Bound for Criterion Value
c = Lower Bound for IVAL Factor
1 = Upper Bound for IVAL Factor
Solution
y = (1– c) e-A (x – a), x ≥ a
where
Criterion Value (x)
IVAL Factor (y)
a
x1
0
c
y1
1
A =
In (1– c) ) – ln y1
x1 – a

## Slide 69: Exponential Curve Formulas
Case 2b: [c, d] = [0, 1]
Knee of Curve at 0.2
Givens
(x1, 0.2) = Point of Diminishing Returns
a = Lower Bound for Criterion Value
c = 0 = Lower Bound for IVAL Factor
d = 1 = Upper Bound for IVAL Factor
Solution
y = e-A (x – a), x ≥ a
where
Criterion Value (x)
IVAL Factor (y)
a
x1
0
0.2
1
A =
In 5
x1 – a

## Slide 70: Exponential Curve Formulas
Case 3: Finite Interval [a, b]
Increasing Function
Givens
(x1, y1 ) = Point of Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = Lower Bound for IVAL Factor
d = Upper Bound for IVAL Factor
Solution
y = d – (d – c) , a ≤ x ≤ b
where
Criterion Value (x)
IVAL Factor (y)
a
x1
0
c
y1
d
b
b – a
b – x - A
A =
In (d – c) – ln (d – y1)
In (b – x1) – ln (b – a)

## Slide 71: Exponential Curve Formulas
Case 3a: Upper bound of unity
Givens
(x1, y1 ) = Point of Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = Lower Bound for IVAL Factor
1 = Upper Bound for IVAL Factor
Solution
y = 1 – (1– c) , a ≤ x ≤ b
where
Criterion Value (x)
IVAL Factor (y)
a
x1
0
c
y1
1
b
b – a
b – x -A
A =
In (1– c) – ln (1 – y1)
In (b – x1) – ln (b – a)

## Slide 72: Exponential Curve Formulas
Case 3b: [c, d] = [0, 1]
Knee of Curve at 0.8
Givens
(x1, 0.8) = Point of Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = 0 = Lower Bound for IVAL Factor
d = 1 = Upper Bound for IVAL Factor
Criterion Value (x)
IVAL Factor (y)
a
x1
0
0.8
1
b
Solution
y = 1 – , a ≤ x ≤ b
where
b – a
b – x -A
A =
In 5
In (b – x1) – ln (b – a)

## Slide 73: Exponential Curve Formulas
A04-12368120
Case 4: Finite Interval [a, b]
Decreasing Function
Givens
(x1, y1 ) = Point of Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = Lower Bound for IVAL Factor
d = Upper Bound for IVAL Factor
where
A =
In (d - c) – ln (y1 - c)
ln (b - x1) – ln (b - a)
Criterion Value (x)
IVAL Factor (y)
a
x1
0
c
y1
d
b
Solution
y = (d – c) + c, a ≤ x ≤ b
b – a
b – x - A

## Slide 74: Exponential Curve Formulas
A04-12368120
Case 4a: Upper bound of unity
Givens
(x1, y1 ) = Point of Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = Lower Bound for IVAL Factor
1 = Upper Bound for IVAL Factor
where
A =
In (1– c) – ln (y1 - c)
ln (b - x1) – ln (b - a)
Criterion Value (x)
IVAL Factor (y)
a
x1
0
c
y1
1
b
Solution
y = (1– c) ) + c, a ≤ x ≤ b
b – a
b – x - A

## Slide 75: Exponential Curve Formulas
In 5
ln (b - x1) – ln (b - a)
b – a
b – x - A
Case 4b: [c, d] = [0, 1]
Knee of Curve at 0.2
Givens
(x1, 0.2) = Point of Diminishing Returns
a = Lower Bound for Criterion Value
b = Upper Bound for Criterion Value
c = 0 = Lower Bound for IVAL Factor
d = 1 = Upper Bound for IVAL Factor
Criterion Value (x)
IVAL Factor (y)
a
x1
0
0.2
1
b
where
A =
Solution
y = , a ≤ x ≤ b